## Slide 1: Electromagnetic Oscillations and Alternating Current Session 12-13
SCIE6063
COMPUTATIONAL PHYSICS
June 2024

## Slide 2
LC Oscillations, Qualitatively
In RC and RL circuits the charge, current, and potential difference grow and decay exponentially.
On the contrary, in an LC circuit, the charge, current, and potential difference vary sinusoidally with period T and angular frequency w.
The resulting oscillations of the capacitor’s electric field and the inductor’s magnetic field are said to be electromagnetic oscillations.

## Slide 4
The energy stored in the electric field of the capacitor at
any time is where q is the charge on the
capacitor at that time.
The energy stored in the magnetic field of the inductor at
any time is where i is the current through
the inductor at that time.
As the circuit oscillates, energy shifts back and forth from one type of stored energy to the other, but the total amount is conserved.
LC Oscillations,

## Slide 5
The time-varying potential difference (or voltage) vC that exists across the capacitor C is
To measure the current, we can connect a small resistance R in series with the capacitor and inductor and measure the time-varying potential difference vR
across it:
LC Oscillations,

## Slide 6
The Electrical Mechanical Analogy:
One can make an analogy between the oscillating LC system and an oscillating block–spring system.
Two kinds of energy are involved in the block–spring system. One is potential energy of the compressed or extended spring; the other is kinetic energy of the moving block.
Here we have the following analogies:
LC Oscillations

## Slide 7
LC Oscillations,
The Block-Spring Oscillator:

## Slide 8
The LC Oscillator:
LC Oscillations,

## Slide 9
Angular Frequencies:
LC Oscillations,
But
The angular frequency of oscillation for an ideal (resistanceless) LC is:

## Slide 10
The electrical energy stored in the LC circuit at time t is,
The magnetic energy is:
But
Therefore
Note that
The maximum values of UE and UB are both Q2/2C.
At any instant the sum of UE and UB is equal to Q2/2C, a
constant.
When UE is maximum, UB is zero, and conversely.
LC Oscillations,

## Slide 11
Example, LC oscillator, potential charge, rate of current change

## Slide 12
2. Damped Oscillations in an RLC Circuit:
Fig. 1. A series RLC circuit. As the charge contained in the circuit oscillates back and forth through the resistance, electromagnetic energy is dissipated as thermal energy, damping ( decreasing the amplitude of) the oscillations.
R
L
C

## Slide 13
Analysis:
Where
And
Damped Oscillations in
an RLC Circuit: (cont.)

## Slide 14
3. Alternating Current
wd is called the driving angular frequency, and I is the amplitude of the driven current.
The basic mechanism of an alternating-current generator is a conducting loop rotated in an external magnetic field.
In practice, the alternating emf induced in a coil of many turn of wire is made accessible by means of slip rings attached to the rotating loop. Each ring is connected to one end of the loop wire and is electrically connected to rest of the generator circuit by a conducting brush against which the ring slips as the loop (and it) rotates
Fig.2. An alternating-current generator

## Slide 16
4. Three Simple Circuits:
(1). A Resistive Load:
For a purely resistive load the phase constant f= 0°.
Fig. 3. A resistor is connected across an alternating-current generator
ε- vR = 0 vR = εm Sin ωdt = VR Sin ωdt

## Slide 17
Gb.4. A Diagram Phasor of VR and IR
VR
vR
IR
iR
ωd
Rotation of phasor
at rate ωd
Three Simple Circuits

## Slide 18
Example, Purely resistive load: potential difference and current
In the figure, resistance R is 200 Ω and sinusoidal alternating emf device operates at amplitude ϵm= 36 V and frequency fd=60,0 Hz.
What is the potential difference vR(t) across the resistance as a function of time t and what is the amplitude VR of vR(t)?
Three Simple Circuits
Fig. 5. A resistor is connected across an alternating-current generator

## Slide 19
(2). A Capacitive Load:
XC is called the capacitive reactance of a capacitor. The SI unit of XC is the ohm, just as for resistance R.
Fig. 6. A capacitor is connected across an alternating-current generator
Three Simple Circuits:

## Slide 20
Three Simple Circuits:

## Slide 21
Fig.7. (a) The current in the capacitor leads the voltage by 900 (π/2 rad)
(b) A phasor diagram shows the same thing.
Three Simple Circuits:

## Slide 22
Example, Purely capacitive load: potential difference and current
In the figure, capacitance C is 15,0 µF and the sinusoidal alternating emf device operates at amplitude εm =36,0 V and frequency fd=60,0 Hz.
a). What are the potential difference vC(t) across the capacitance and the amplitude VC of vC(t)?
b). What are the current iC(t) in the circuit as a function of time and the amplitude IC of iC(t) ?
Three Simple Circuits:

## Slide 23
(3). An Inductive Load:
Three Simple Circuits
Fig. 8. An inductor is connected across an alternating current generator
VL
iL
ε
L
~
Notes: is the ohm,

## Slide 24
Three Simple Circuits:
Fig.9. (a) The current in the inductor lags the voltage by 900(=π/2 rad). (b) A phasor diagram shows the same thing.
Rotation of phasors at rate ωd
ωd
VL
IL
iL
vL

## Slide 25
Example, Purely inductive load
In fig. Inductance L is 230 mH and the sinusoidal alternating emf device Operates at amplitude εm =36 V and frequency fd = 60 Hz.
What are the potential difference VL(t)?
What are the current iL(t) in the circuit as a function of time
and the amplitude I of iL(t)?
Three Simple Circuits:
VL
iL
L
ε
~
Fig. 10. An inductor is connected across an alternating current generator

## Slide 26
Circuit Element | Symbol | Resistance or Reactance | Phase of Current | Phase Constant (or angle) ф | Amplitude Relation
Resistor | R | R | In phase with VR | 00(=0 rad) | VR=IR R
Capacitor | C | XC= 1/(ωdC) | Leads VC by 900 (=π/2 rad) | -900(=-π/2 rad) | VC=IC XC
Inductor | L | XL= ωdL | Lags VL by 900 (=π/2 rad) | +900(=+π/2 rad) | VL=IL XL
Table 1. Phase and Amplitude Relations for Alternating currents and Voltages

## Slide 27
5. The Series RLC Circuit
Fig. 11. (a) A phasor representing the alternating current in the driven RLC circuit at time t. The amplitude I, the instantaneous value i, and the phase(wdt -f) are shown. (b) Phasors representing the voltages across the inductor, resistor, and capacitor, oriented with respect to the current phasor in (a).

## Slide 28
Fig.11.
(c) A phasor representing the alternating emf that drives the current of (a).
(d) The emf phasor is equal to the vector sum of the three voltage phasors of (b).Here, voltage phasors VL and VC have been added vectorially to yield their net phasor (VL-VC).
The Series RLC Circuit
(d)
(c)

## Slide 29
The Series RLC Circuit

## Slide 30
The Series RLC Circuit

## Slide 31
6. Power in Alternating Current Circuits:
The instantaneous rate at which energy is dissipated in the
resistor:
The average rate at which energy is dissipated in the resistor,
is the average of this over time:
Since the root mean square of the current is given by:
Similarly,

## Slide 32
Where
Power in Alternating Current
Circuits (cont.)

## Slide 33
A series RLC circuit, driven with εrms=120 V at frequency fd=60 Hz, contains a resistance R=200 Ω, an inductance with inductive reactance XL=80 Ω, and a capacitance with capacitive reactance XC= 150 Ω.
What are the power factor cosф and phase constant ф of the circuit?
What is the average rate Pavg at which energy is dissipated in the resistance?
What new capacitance Cnew is needed to maximize Pavg if the other parameters of the circuit are not changed?
Example,
Driven RLC circuit:

## Slide 34
Assignment
Do the problems in the text-book:
Fundamental of Physics, Chapter 31 (Electromagnetic Oscillation and Alternating Current); p.935-940
Problems No. 3, 13, 29, 44, 53, 59, and 68

## Slide 35
Bina Nusantara
These slides have been adapted from Halliday D.; Resnick R. and Walker J. (2018). Fundamentals Of Physics ,Extended,
11th , John Wiley & SONS Inc, New York, ISBN: 9781119306856
Chapter 31